SPECIFICATIONS, QUALITY AND STANDARD:   MAZUT 100 GOST–10585-75

## GUARANTEED SPECIFICATION OF RUSSIAN MAZUT 100 GOST–10585-75

|  | COMPONENT |  | RESULT |
| --- | --- | --- | --- |
| 1. | Ash content, not more % |  | 0.14 |
| 2. | Mass fraction of sulphur, not more % | low sulphur residual oil | 0.5 |
| 3. | Temperature of the flash, not less ℃ | in the closed crucible | 65 |
|  |  | in the open crucible ℃ | 110 min |
| 4. | The temperature of solidification, not higher ℃ |  | 25 |
| 5. | Kinematics viscosity |  | 118 max |
| 6. | Water content |  | 0.5% |
| 7. | Mechanical impurities |  | Lower than 0.1% |
| 8. | Acidity |  | Lower than 5 mg KOH/ 100ml |
| 9. | Alkalinity |  | nil |
| 10. | Gross Calorific Value Kcal/kg / KJ/kg |  | Min9200/41300 |
| 11. | Density at 15.0 deg. C Kg/l |  | 0.8900-0.9200 |
| 12. | Hydrogen Sulfide Content (H2S) pom |  | 0.5 max |
| 13. | Carbon Residual |  | Lower than 7% |
| 14. | Vanadium (V) ppm |  | 23 |
| 15. | Aluminium (Al) ppm |  | 5 |
| 16. | Silikon (Si) ppm |  | 12 |
| 17. | Nickel (Ni) ppm |  | 29 |
| 18. | Asphaltenes m/m |  | 3.6% |
| 19. | Destilation @4 mm Hg Extracted to 760 mm Hg |  |  |
|  |  | Initial Boiling Point deg. C | 216 |
|  |  | 5% recovered deg. C | 259 |
|  |  | 10% recovered deg. C | 310 |
|  |  | 20% recovered deg. C | 358 |
|  |  | 30% recovered deg. C | 445 |
|  |  | 40% recovered deg. C | 502 |
|  |  | 50% recovered deg. C | 534 |
|  |  | 60% recovered deg. C | 538 |
|  |  | 75% recovered deg. C | 545 |
|  |  | 80% recovered deg. C | - |
|  |  | 90% recovered deg. C | - |
|  |  | Final Boiling point deg. C | 550 |
|  |  | Percent Recovered vol | 78% |
|  |  | Residu vol | 22% |
|  |  | Total Nitrogen m/m | 0.192% |
| 20. | Sodium (Na) ppm |  | 15 |