UREA Specifications:

# PRILLED UREA

QUALITY SPECIFICATIONS:                   	:	WHITE PRILLED

MASS PART NITROGEN 	:	46.2%

BIURET, NOT MORE THAN	:  	1.0%

MOISTURE NOT MORE THAN	:  	0.5%

GRANULOMETRY: (GRANULES SIZE)  	:   	1mm to 4mm 90% min.

FREE AMMONIA:                                        :  	160 PXT PPM MAX.

MELTING POINT:                                        :   	32 DEGREES CEN.

CRUMBLINESS:

PHYSICAL   PROPERTIES	:	NON RADIOACTIVE

WHITE, FREE FLOWING, FREE FROM

HARMFUL SUBSTANCES, 100%

TREATED AGAINST CAKING

# GRANULATED UREA

QUALITY SPECIFICATIONS	:     WHITE GRANULES

NITROGEN RECALCULATED TO DRY  	: 	46.2%

BIURET, NOT MORE THAN	:  	1.0%

WATER, NOT MORE THAN  	:  	0.5%

GRANULOMETRY: (GRANULES SIZE)  	:  	2mm to 4mm 90% min.

FREE AMMONIA:                                        :	160 PXT PPM MAX.

MELTING POINT:                                        : 	132 DEGREES CEN.

CRUMBLINESS	:     100%

PHYSICAL   PROPERTIES	:	NON RADIOACTIVE

WHITE, FREE FLOWING, FREE FROM

HARMFUL SUBSTANCES COATED,

SPHERICAL & UNIFORM IN SIZE, 100%

TREATED AGAINST CAKING

UREA – Defined

Urea is a white dry organic compound and a crystalline substance and has minimum of 46% Nitrogen calculated in dry state. This has the melting point of 132 deg F.

CHEMICAL FORMULA FOR UREA:

CO(NH2)2 or NH2CONH2