SPECIFICATIONS, QUALITY AND STANDARD:   DIESEL AUTOMOTIVE GAS OIL (AGO)

## GUARANTEED SPECIFICATION OF RUSSIAN DIESEL AUTOMOTIVE GAS OIL (AGO)

| PARAMETER | TEST METHOD IP/ASTM | LIMITS |
| --- | --- | --- |
| Specific Gravity 15/15 deg C | 160 / D1298 | 0.820min, 0.870 max |
| Distillation: Recovered @ 357 deg C (% Vol. EBP deg.) | 123 / D86 | 90 min, 385 max |
| Color (ASTM) | D 150000 | 3 max |
| Flash Point (deg. C) | 34 / D93 | 66 |
| Total Sulphur ( % wt) | x-ray | 0.3 max |
| Copper Corrosion (3 hr @ 100 deg. C) | 154 / D130 | No. 1 Strip max |
| Kinematic Viscosity @ 38 deg. C (Cst) | 71 / D445 | 1.6 – 5.5 |
| Cloud Point (deg. C) | 219 / D2500 | 4.4 max |
| Carbon residue (% wt.) | D189 | 0.15 max |
| Acidity (inorganic acid) |  | Nil |
| Total Acid Number (mg KOH/gm) | 139 / D974 | 0.50 max |
| Ash Content (% wt.) | 4 / D482 | 0.01 max |
| Sediment (% wt.) | 53 / D473 | 0.01 max |
| Water by Distillation | 74 / D95 | 0.05% max |
| Diesel Index | IP 21 | 47 min |